## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 2

## Slide 3: OSI Reference Model - Reminding
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 4: Signals
Continious - Analog
Discrete - Digital
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 5: Signals – Con’t
Periodic
Non-periodic
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 6: Analog Signals
Simple Analog Signals
Complex Analogue Signals
v – Amplitude
  Volt - V
  Amper - A
  Watt-W
f – Frequency
  Cycle
  Hertz - Hz
 - Phase
  Degree - 
  Radian - 
Frequency | Time
Hz | sec (second)
KHz | msec (milli second)
MHz | μsec (micro second)
GHz | nsec (nano second)
THz | psec (pico second)
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 7: Analog Signals – Con’t
Frequency Change
Amplitude Change
Phase Change
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 8: Digital Signals
Non-periodic
Bit-rate
  The number of bits transferred in one second
Bit-interval
  The time it takes to transmit one bit (in seconds)
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 9: Elements that Negatively Affect Communication
Distortion
  Attenuation
    dB
    Solution: Amplifying
      Analog?
  Noise
    Even Idle mode
    Thermal noise
      Motion of atomic fragments
    Impulse noise
      Random electromagnetic signal
  Cross talk
  Delay
  Propagation: Velocity of a sinusoidal signal in a transmission line
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 10: Data Carrying Capacity
Nyquist Theorem
  The amount of data that can be sent per unit time
  H: Band width
  V: Number of discrete voltages
  Not consider the noise
Noise (dB)
  Signal strength (sent): S
  Strength of the current noise: N
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 11: Data Carrying Capacity – Con’t
Shannon-Hartley
  Data velocity with noise
First, the highest data rate to be achieved is found according to the Shannon-Hartley formula.
Then, according to the Nyquist formula, how many discrete voltage levels can be used in this bandwidth is determined.
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 12: Example
Since it is known that the SNR value on a transmission channel between 3KHz-4KHz is 24dB, what is the maximum rate that can be obtained and the number of discrete levels that can be used for transmission?
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 13: Coding of Signals
Digital – Digital
  Computer – Printer
Analog – Digital
  Microphone – Computer
Digital – Analog
  Computer – Communication Lines
Analog – Analog
  Radio – Radio Signal Lines
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 14: Digital – Digital Coding
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 15: Digital2Digital – Unipolar Coding
2 main problems;
  DC Component
  Synchronization
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 16: Digital2Digital – Polar Coding
3 main types
  Non Return to Zero (NRZ)
    Non Return to Zero-Level (NRZ-L)
    Non Return to Zero-Inverted (NRZ-I)
  Return to Zero (RZ)
  Biphase
    Best Digital2Digital Technique
    Manchester
    Differential Manchester
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 17: Digital2Digital – Bipolar Coding
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 2
3 voltage levels
  (+, - and 0) like RZ
  0V 0
  +, - 1
  AMI (Alternate Mark Inversion)
  B8ZS (Bipolar 8 Zero Synchronizing)
  HDB3 (High Density Bipolar 3)
If the number of 1s transferred after the last conversion is odd
If the number of 1s transferred after the last conversion is even
Data before the HDB3 Coding is even
Data before the HDB3 Coding is odd

## Slide 18: Analog – Digital Coding
PAM (Pulse Amplitude Modulation)
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 19: Analog – Digital Coding – Con’t
PCM (Pulse Code Modulation)
BLM3051
Data Communication and Computer Network - 3
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 20: Analog – Digital Coding - Nyquist Theorem
Sampling at least twice the highest frequency component is required
Example:
  If bandwith is 1000-4000Hz, sampling fre. must be 8000
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 21: Transmission of the Analog Signal over the Digital Network
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 22: Digital – Analog Coding
ASK (Amplitude Shift Keying)
FSK (Frequency Shift Keying)
PSK (Phase Shift Keying)
  It is not affected by voltage additions caused by external environment effects such as ASK, and bandwidth related problems such as FSK.
QAM (Quadrature Amplitude Modulation)
  PSK ASK
4 phase + 2 amp.
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 23: Analog – Digital Coding - Concepts
Carrier Signal
Bit and Baud Speed
  Bit Speed ≥ Baud Speed
Coding Technique | Unit | Baud Speed | Bit Speed | Bits / Baud
ASK, FSK,2PSK | Bit | N | N | 1
4PSK, 4QAM | Dibit | N | 2N | 2
8PSK, 8QAM | Tribit | N | 3N | 3
16QAM | Quadbit | N | 4N | 4
32QAM | Pentabit | N | 5N | 5
64QAM | Hexabit | N | 6N | 6
128QAM | Septabit | N | 7N | 7
256QAM | Octabit | N | 8N | 8
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 24: Analog – Analog Coding
AM (Amplitude Modulation)
FM (Frequency Modulation)
PM (Phase Modulation)
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 25: Digital Data Transmission Techniques
Medium specs;
  Connector type to provide mechanical connection in the transmission medium
  Number of wires
    Signal type
    Purpose
  Frequency, amplitude and phase
Parallel Transmission
Serial Transmission
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 26: Parallel Transmission
1
Ø
1
Ø
N Wired Connection
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 27: Parallel Transmission – Con’t
Standard Parallel Interface
  155 kByte/sec
ECP/EPP (Enhanced Parallel Port/Enhanced Capability Port)
  3 MByte/sec
Maximum Cable Length: 7.5m
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 28: Parallel Transmission – Con’t
Laplink
Interlink
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 29: Serial Transmission
1
Ø
1
Ø
1
1
Ø
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 30: Serial Transmission – Con’t
RS–232-C
  9 wires
    RX
    TX
    GND
    6 x Flow Control Wire
  155 kbits/sec
  15 meters
  NRZ-L
    (-15~-5)VDC1
    (+5~+15)VDCØ
  RS–422: 300 meters
Asynchronous transmission in WAN
  2 wires
Synchronous transmission in WAN
  4 wires
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 31: Asynchronous Serial Transmission
Simple, Cheap
The data arrival rhythm between the sides is not the same.
It is not possible to tell when the incoming transmission started and when it ends
Receiver and transmitter must agree on how long each bit will remain on the line.
Start bit: 0, positive voltage
  8-N-1
    1 + 8 + 1 -> LSB
    N: not parity bit
  7-E-1
    1 + 7 + 1 (Even)
Stop bit: 2-bits long
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 32: Asynchronous Serial Transmission – Con’t
Since the communication between the sender and receiver is not made simultaneously, there are gaps of variable duration between the bytes sent.
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 33: Asynchronous Serial Transmission – Con’t
Time skew
  If the processing speed difference between the two sides is 5%
    8th -> 45%
Dial-up
  Carrier Signal
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 34: Synchronous Serial Transmission
Much more big data transfer compare to Async within one transmission (>1000 byte)
If there is no data transmission
  A special bit sequence is sent in the line.
In order for the information to be transferred properly, operations must be carried out depending on a common timing mark.
Like an assembly line.
Clock line: A different line
  Clock pulse
  Short distance transmissions
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 35: Synchronous Serial Transmission – Con’t
Logical Level Synchronization
  Preamble Bit Array
  Postamble Bit Array
  Max 100 bits for control data.
  HDLC (High Level Data Link Control)
    48 bits for control purposes.
    Example
      If we want to transfer 1000 characters in HDLC mode, how much bits send?
        1 character → 8 bit
        1000 characters → 1 block
        Control data → 48-bit
        1 block → 8000 bit
        8000 + 48 → 8048 bits
        Load of control data per bloc → 48 / 8048 ≈ 0,6%
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 36: Asynchronous ST vs Synchronous ST
Synchronous | Asynchronous
Much more efficient usage Better error control High transmission speed | Simple Cheap Additional effort required for timing Limited speed Limited error control mechanism (parity) 20% loss due to start / end bits
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 37: Thank you for your listening.
BLM3051
Data Communication and Computer Network - 2
Dr. Öğr. Üyesi Furkan ÇAKMAK