## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 4

## Slide 3: DTE-DCE Interfaces
DCE (Data Circuit-Terminating Equipment)
  Modem
DTE (Data Terminal Equipment)
  Computer
  Printer
  Fax
  etc.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 4: DTE-DCE Interfaces – Con’t
Standards between DTE and DCE
  EIA
    EIA–232
    EIA–442
    EIA–449
  ITU-T
    V.24
    V.32
    V.32bis
    V.34
    X.2
    X.24
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 5: Transmission Medium
Wire
Light
Radio Wave
Guided and Unguided media
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 6: Guided Media
Coaxial Cable
  AUI (Attachement Unit Interface)
  Ethernet
  Thick: 10mm
  Thin: 5mm
Twisted pair
  DGM (Data Grade Medium)
  CATs
  2-12 twist/step
  Different Colors
  There are 3 different types:
    UTP (Unshielded Twisted Pair)
      100m = 90m + 10m
    ScTP/FTP (Screened Twisted Pair/Foiled Twisted Pair)
    STP (Shielded Twisted Pair)
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 7: Guided Media – Con’t
UTP cables category criterias:
  Signal Frequency
  Wire lenght
  Correct connections
  Attenuation
  NEXT (Near-End Crosstalk)
  PSNEXT (Power Sum NEXT)
  FEXT (Far-End Crosstalk)
  ELFEXT (Equal Level FEXT)
  PSELFEXT (Power Sum ELFEXT)
CAT 5e
  gigabit Ethernet
  4 pieces of 2
  Propagation delay
    Skew
      Fastest - Slowest
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 8: Classification of UTP Cables
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 9: Guided Media – Fiber Optic Cabels
Coaxial Cables
Twisted Pair Cables
Fiber Optic Cables
  300.000 km/sec
  >= 100 Gbps (reached 500 Gpbs)
  Core
  Cladding
  Primary buffer
  Secondary buffer
  Armor
  Plastic Shield
SMF (Single Mode Fiber)
MMF (Multi Mode Fiber)
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 10: Guided Media – Fiber Optic Cabels – Con’t
Single Mode Fiber (SMF)
  Core: 9 μm
  Light wavelength: 1.3 – 1.5 μm
  1.3 μm 9 μm Transmission is carried out as a single, unbreakable beam
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 11: Guided Media – Fiber Optic Cabels – Con’t
Step Index
Grade Index
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 12: Guided Media – Fiber Optic Cabels – Con’t
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 13: Guided Media – Fiber Optic Cabels – Con’t
Light sources used in fiber optic media:
  LED (Light Emitting Diode)
    Nonfocusable
  ILD (Injection Laser Diode)
    Focusable
  Receiver side: fotodiod (Photosensitive cell)
    It is a circuit element that can generate electrical signals depending on the strength of the light falling on it.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 14: Advantages of Fiber Optic Cables over Copper Cables
Broad Bandwidth
Immunity to Electromagnetic Interference
Attenuation
Insulation
Space Saving
Security
  Eavesdrop
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 15: Things to Consider When using Fiber Optic Cables
The core parts of the fibers used at both ends must overlap exactly.
  Attention should be paid to dirt, oil, dust and scratches.
  Dirt, dust, etc. should be cleaned with air gun or alcohol.
  Scratches should be polished and rounded.
Fiber cables are fragile like glass and must be kept gently bent.
When not in use, fiber cables should be stored with special headers to protect them from dust and scratches.
The laser beam at the end of the fiber optic cable is dangerous to the eyes.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 16: Unguided Media
Technologies that aim to use the atmosphere:
  RF (Radio Frequency)
  Microwave
  IR (Infra Red)
Ionosphere
  Ground propagation < 2 MHz
  Sky propagation 2-30 MHz
  Line of sight propagation > 30 MHz
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 17: Unguided Media - Radio Frequency
  3 kHz – 1 GHz
  Television ve Radio
  Omnidirectonal
  Antennas do not need to be aligned
  RF can go through the Wall.
  Obtain approval from authorities to use RF.
  Non-approval RF types:
    Bluetooth, IEEE 802.11, etc.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 18: Unguided Media - Microwaves
  1-300 GHz
  Satellite - Ground Station
  Parabolic and horn antennas
    Unidirectional
    LOS – Line Of Sight
  Microwaves can not go through the Wall
  It can be harmful to the living creature between the transceiver, depending on the signal strength used.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 19: Unguided Media - Infra Red
  300GHz-400THz
  Point-to-point
    Device’s remotes
  Infra Red can not go through the Wall
  Tapping-eavesdropping
  Jamming Immune
  75 kbps in max. 8m distance
    Top: 4 Mbps
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 20: Comparison of Transmission Medium
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 21: Could There be an Alternative Option in Data Transmission?
  300GHz-400THz
  Point-to-point
    Device’s remotes
  Infra Red can not go through the Wall
  Tapping-eavesdropping
  Jamming Immune
  75 kbps in max. 8m distance
    Top: 4 Mbps
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 22: Multiplexing
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 23: Multiplexing Technics
FDM (Frequency Division Multiplexing)
WDM (Wavelength Division Multiplexing)
TDM (Time Division Multiplexing)
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 24: FDM (Frequency Division Multiplexing)
Each signal has a different carriage signal
  The signal to be sent is the sum of the carrier signals
  Voice: 300-3300Hz BW
  Guarded Band
Television and radio broadcasts
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 25: WDM (Wavelength Division Multiplexing)
Like FDM in FO
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 26: TDM (Time Division Multiplexing)
2 Types
  Synchronous TDM
    Data
    Digitized Voice
  Asynchronous TDM
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 27: Synchronous TDM
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 28: Synchronous TDM – Con’t
Example
  In Sync. TDM where 4 units are connected, each unit produces 250 characters / sec output.
  1 bit is used for each frame to ensure synchronization.
  Each frame contains a character from each unit.
  Accordingly, calculate the obtained data communication speed as bps.
Answer:
  250 frame + 250 bit (for sync.)
  250 frame x (4 unit x 8 bits/unit) / frame + 250 bit = 8250 bps
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 29: Asynchronous TDM
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 30: Error Detection and Correction Techniques
Data Link Layer (in OSI model)
Error reasons
  Attenuation
  Delay Distortion
    Video + Voice
    Problem in time sensitive conditions
  Noise in the communication environment
    Thermal noise
      Random electron motion
    Intermodulation noise
    CrossTalk
    Impulse Noise
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 31: Error Types
Single bit error
Multi bit error
Error bursts
1 | Ø | Ø | Ø | Ø | 1 | 1 | 1
1 | Ø | 1 | Ø | Ø | 1 | 1 | 1
Data Sent
Data Received
1 | Ø | Ø | Ø | Ø | 1 | 1 | 1
1 | Ø | 1 | Ø | Ø | Ø | 1 | 1
1 | Ø | Ø | Ø | Ø | 1 | 1 | 1
1 | Ø | Ø | 1 | 1 | Ø | Ø | 1
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 32: Error Detection
Both sides have original data?
Sending data twice?
Control block?
  4 different types
    VRC (Vertical Redundency Code)
    LRC (Longitudial Redundency Code)
    CRC (Cyclic Redundency Check)
    Checksum
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 33: VRC (Vertical Redundency Code)
Parity check
Simple error coding technique
The number of errors should be odd.
XOR operation
Data Sent
Data Received 1
Data Received 2
Data Received 3
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 34: LRC (Longitudial Redundency Code)
LRC is 2D-VRC
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 35: CRC (Cyclic Redundency Check)
The data to be sent is divided into a predetermined prime polynomial.
The remainder value is added to the data to be sent as an error control code.
The remainder zero in receiver side means that error-free transmission.
Common polynomials used for CRC: 13-bits, 17-bits, 33-bits
  The number of undetectable errors is almost zero
Commonly used polynomials in CRC technique:
  CRC-12 x12+x11+x3+x+1
  CRC-16 x16+x15+x2+1
  CRC-ITU x16+x12+x5+1
  CRC-32 x32+x26+x23+x22+x16+x12+x11+x10+x8+x7+x5+x4+x2+x+1
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 36: CRC (Cyclic Redundency Check) - Con’t
Example: Data Sent: 100100, polynom: x3 + x2 + 1, CRC = ?
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 37: Checksum
The sender divides the data into N-bits parts (usually 16 bits are used).
The parts are collected using the first complementary arithmetic.
  In this way, a total value of only N bits is obtained.
Calculate two's complement using summed value
  The calculated value is added to the end of the information to be sent.
The checksum detects all of the odd errors and most of the even numbers.
  However, if one or more bits in a part are 0 when they are 1, but there is a 0 when 1 in another part, the error will not be understood because there will be no difference in this column sum.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 38: Checksum - Con’t
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 39: Error Correction
2 methods
  Send data again
  If one bit error
    Hamming Code / Distance
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 40: Hamming Code
If we sent m bit data, the error occurs in 1,2,…,m bit
Adding error-free state, the data length will be m+1
Control block length must be
bit must be sent error-free
So, control block length must be
(1, 2, 4, 8, 16. bits)
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 41: Hamming Code – Con’t
BLM3051
Data Communication and Computer Network - 4
R1=B1B3B5B7B9B11
R2=B2B3B6B7B10B11
R3=B4B5B6B7
R4=B8B9B10B11
R1=B3B5B7B9B11 = 10101 = 1
R2=B3B6B7B10B11 = 11101 = 0
R3=B5B6B7 = 011 = 0
R4=B9B10B11 = 001 = 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 42: Thank you for your listening.
BLM3051
Data Communication and Computer Network - 4
Dr. Öğr. Üyesi Furkan ÇAKMAK