## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 3: Data Link Control
Basic tasks of the data link layer:
  Framming and determining of start and end points to ensure synchronization
  Flow control
  Error control / Retransmission
  Addressing
  Line dicipline / Link management
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 4: Line Dicipline / Link Management
Enq/Ack (Enquiry/Acknowledgement)
Poll/Select Connection Management
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 5: Enq/Ack (Enquiry/Acknowledgement)
Point to point (in WANs)
Units are expected to have equal properties
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 6: Poll/Select Connection Management
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Multi-point (in LANs)

## Slide 7: Flow Control
Overwhelm
Buffer
There are two basic techniques:
  Stop & Wait
  Sliding Window
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 8: Stop & Wait
ACK is required for every transfer.
Pros:
  Packages consist of smaller pieces
  Effective use of buffers
  Medium is busy for a shorter time
  Error probability decreases
  Error control processing times are shortened.
  Wait time may be shorter for other devices in LANs.
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 9: Stop & Wait – Line Utilization (U) Rate
tframe: Transmission time of a single frame
tprop: The time it takes from the sender to the receiver
tack: The time it takes for all bits of the ACK to exit the receiver
TF = tframe+ tprop+ tack+ tprop
TF = tframe+ 2tprop
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 10: Stop & Wait – Line Utilization (U) Rate – Con’t
Example:
  Data communication is made between two points at a distance of 1000 km (d = 1000 km = 106 m) at a speed of 155.52 Mbps (R=155.52 106 bit/sec).
  The transmission speed of the line is 200.000.000 m/sec (V=2 108 m/sec).
  Frame size is 424 bits (L = 424 bit).
  What is the Line Utilization (U) in Stop & Wait Flow Control mode?
Answer
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 11: Sliding Window
U rate is low in Stop & Wait
The sender sends a certain amount of data to the receiver without ACK data.
Frames are transmitted in convoys.
The receiver can send ACK data for several frames.
Frame number is necessary
  n-bit frame
Piggy backing
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 12: Sliding Window – Sender Side
Window size: 2n-1
  Example: If frame sequence number bit length is n=3, windows size is 2n-1 = 7
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 13: Sliding Window – Receiver Side
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 14: Sliding Window – Both Side Example
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 15: Sliding Window – Window Size 2n-1
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 16: Sliding Window - Line Utilization (U) Rate
In Stop & Wait
In Sliding Windows
If w (window size)  (2a +1)
  U = %100
If w < (2a+1)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 17: Error Control, Automatic Repeat reQuest (ARQ)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 18: Stop & Wait ARQ
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 19: Sliding Window ARQ
There are some differences caused by the sliding window technique when the frames inside the window are sent without a receipt.
  The sender continues to store the frames in the buffer until it receives ACK for the frames.
  In the ACK / NACK information coming from the receiver, there will be a number field showing which numbered frame it is for.
  Receive Ready
    RR 3 and RR 6 means: I have received 3, 4, 5 numbered frames, waiting for frame 6.
  Each faulty frame is immediately reported by the receiver to the sender.
    REJ - Reject
    SREJ – Selective Reject
  The sender also has a timer in the sliding window approach.
    Lost data frame
    Lost acknowledge frame
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 20: Sliding Window – Go Back n ARQ
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 21: Sliding Window - Selective Reject / Selective Repeat ARQ
In this technique, the receiver will receive the frames unordered.
  Search and Sort Algorithms are necessary.
  Processing complexity increases
    In Go Back n: w = (2n–1)
    In Selective Reject: w ≤ (2n+1)/2
  SREJ
  The receiver accepts frames without error after faulty frame.
  Frames will come in different order due to faulty frames.
    Duplicated ones
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 22: Sliding Window - Selective Reject / Selective Repeat ARQ - Con’t
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Screen Shot 2020-11-09 at 00.35.20

## Slide 23: Data Link Protocols
Protocol is a set of rules used to perform the necessary operations during data flow.
  Synchronous
  Asynchronous
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 24: Data Link Controls (DTC)
Components
  Software
  Hardware (UART/USART)
Tasks
  Synchronous Transmission
    Physical Level: Common timing signal
    Logical Level: Special bit or bit-arrays
  Flow Control
  Error Control
  Transmission Rules
    Which one is sender/receiver?
    Whether frames are for data or control purposes
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 25: Asynchronous Protocols
Used for connections made with a modem
Logical Sync.
  Start bit
  End bit
There may be gaps of variable sizes between data blocks.
Cons: Additional data
Cons: Slow transmission
Most Common Examples:
  X-Modem
  Y-Modem
  Z-Modem
  Kermit
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 26: Synchronous Protocols
Instead of start and end bits, FLAGS is used
  Synchronization premise (SYN) bit-arrays
  Synchronization successor (EOT) bit-arrays
2 types:
  Physical Level Synchronization
    Common Clock Signal
  Logical Level Synchronization (in Data Link Layer)
    FLAGs
Thanks to the fast transmission
  Used in LAN, MAN and WAN technologies
The protocol perceives the data sent as a consecutive byte sequence.
  According to the coding system used (ASCII or EBCDIC)
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Synchronization premise: Eşzamanlılık öncülü
Synchronization successor: Eşzamanlılık ardılı

## Slide 27: Synchronous Protocols – Byte Oriented
*Character Oriented
ASCII or EBCDIC coding
2 types of frames
  Control frames
  Data frames
Control Chars | Explanation
SYN | Synchronous idle (makes the channel active)
PAD | Frame PAD (used for completion)
DLE | Data Link Escape (Escape char for control chars)
ENQ | Enquiry (Request)
SOH | Start of Heading
STX | Start of Text
ITB | End of Intermediate Block
ETB | End of Transmission Block
ETX | End of Text
EOT | End of Transmission
BCC | Block Check Count (LRC -> 1 byte, CRC -> 2 bytes)
ACK0 | Acknowledge Even Numbered Blocks
ACK1 | Acknowledge Odd Numbered Blocks
WACK | Wait Before Transmitting
TTD | Temporary Text Delay (While filling buffer in sender side)
RVI | Reverse Interrupt (Request for urgent response)
NUL | (Filling spaces)
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 28: Synchronous Protocols – Byte Oriented – Data Frames
Header includes address
Data Transparency ? (in voice and image data)
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 29: Synchronous Protocols – Byte Oriented – Data Frames
DLE before STX, ETX, ETB, ITB, SOH control chars
If data includes DLE char?
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 30: Synchronous Protocols – Byte Oriented – Data Frames
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 31: Synchronous Protocols – Byte Oriented – Multi Block Frames
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 32: Synchronous Protocols – Byte Oriented –Multi-Frame
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 33: Synchronous Protocols – Byte Oriented – Control Frames
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 34: Synchronous Protocols – Byte Oriented – BSC (Binary Synchronous Communication)
IBM
Used until the late 1960s
General Specs:
  Suitable for point-to-point or multi-point connections
  Half duplex
  Use STOP & WAIT for Flow Control and ARQ
  Code Dependent
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 35: Synchronous Protocols – Bit Oriented
Used more actively than byte oriented protocols
  Fit more information into a shorter frame size
  Less faced with data transparency problem
All bit oriented protocols reference HDLC (High Level Data Link Control)
  ISO
General Specs:
  Suitable for point-to-point or multi-point connection.
  Support Half duplex and Duplex
  Use Sliding Windows for Flow Control and ARQ
  Code Independent
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 36: Synchronous Protocols – Bit Oriented
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 37: Synchronous Protocols – Bit Oriented – HDLC (High Level Data Link Control)
Concepts used in HDLC
  Station types
    Primary
    Secondary
    Combined
  Configuration
    Unbalanced
    Balanced (not defined in HDLC)
  Modes of communication
    NRM (Normal Response Mode): Unbalanced. The usual primary/secondary relationship
    ARM (Asynch. Response Mode): Unbalanced. Secondary station transmit data without primary station's permission if line is available.
    ABM (Asynch. Balanced Mode): Balanced
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 38: Synchronous Protocols – Bit Oriented – HDLC Frame Structure
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 39: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – FLAG Field
Consist of 8-bits
  01111110
Determinin start and end point of frames
Ensure synchronicity
Critical point for data transparency
  Bit stuffing
    Sender add a 0-bit between 1’s (like escape char)
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 40: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – FLAG Field - Bit Stuffing
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 41: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – ADDRESS Field
Contains the address of the secondaries.
Address data is in Network Layer (Third Layer)
  Used to determine whether;
    Is it command? or Is it answer?
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 42: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – CONTROL Field
1 or 2 byte length
  If w=7 in sliding window technique, length is 1
  If w=127 in sliding window technique, length is 2
    In applications with high line delays such as WAN
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 43: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – I-Frame
If w=7;
  Each I-Frame contains 2 three-bit fields for flow an error control.
    N(S): Sequence number of the sending window
      Like ACK
    N(R): Sequence number of the receiving window
      If last frame is error-free, N(R) contains next frame's number
      If last frame has errors, N(R) contains number of faulty frame
If w=127
  Each I-Frame contains 2 seven-bit fields for flow an error control.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 44: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – S-Frame
S-Frame means that neither sides has data to send to the other.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 45: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – S-Frame - RR
It has four basic uses:
  ACK
  POLL
    P=1
  REJECT POLL
    F=1
  ACCEPT SELECT
    F=1
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 46: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – S-Frame - RNR
It has three basic uses:
  ACK
  SELECT
    P=1
    If primary sends RR and P=1, it means POLL.
  REJECT SELECT
    F=1
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 47: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – S-Frame – REJ, SREJ
Used to return negative feedback from the receiver
  REJ: Go Back N ARQ
    It is used to inform the sender that the frame whose number is written in the N (R) field and the frames that come after it did not reach the receiver or that it received incorrectly, and to ensure that it is sent again.
  SREJ: Selective Reject ARQ
    It is used in the N (R) field to inform the sender that the data frame whose number is written on it did not reach the receiver or that it was received incorrectly and to send it again.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 48: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame
Used to provide session control
The data area is used to carry information required for system management functions
1st code field consist of 2 bits
2nd code field consist of 3 bits
25 = 32 different state
These states (commands and answers) can be collected in 5 different categories:
  Mode setting
  Unnumbered exchange
  Disconnection
  Initialization
  Miscellaneous
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 49: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame – Mode Setting
How will the transmission be?
  00-001 (SNRM-Set Normal Response Mode) -> w=7
  11-000 (SARM-Set Async. Response Mode) -> w=7
  11-100 (SABM-Set Async. Balanced Mode) -> w=7
  11-011 (SNRM Extended) -> w=127
  11-010 (SARM Extended) -> w=127
  11-110 (SABM Extended) -> w=127
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 50: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame – Unnumbered Exchange
Data connection information exchange
  00-100 (UP-Unnumbered Poll): POLL request
  00-000 (UI-Unnumbered Info): exchange of date/time information to be used for sync.
    UI would be a command or answer.
      If it is used for command, it transports list of parameters to be used for transmission.
      If it is used for answer, it carries information that determines the capability of the receiver.
  00-110 (UA-Unnumbered Ack): Sent in response to the UP command
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 51: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame – Disconnection
There are 3 types of disconnection command.
  00-010 (DISC): Sent by the first side to terminate the connection to the other.
  00-010 (RD): It is used to notify the request to terminate the connection from the second station to the first.
  11-000 (DM): When the address is sent from the specified station to the station wishing to establish the connection, it is sent as negative feedback information to the mode setting command.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 52: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame – Initialization
Used for initializations for all sides.
  10-000 with P (SIM-Set Initialization Mode)
    Command is sent from the first station to the second
    UI command will be sent in response to SIM command
  10-000 with F (RIM-Request Initialization Mode)
    It means that «I am waiting SIM commad»
    It is used when the second station cannot respond to the mode setting command without receiving the SIM command from the first.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 53: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – U-Frame – Miscellaneous
11-001 (RESET)
  This is usually sent in response to a received FRMR code.
  Explains that the secondary station must do the same
11-101 (XID)
  Emphasizes that a self-determining information is requested from the secondary station.
  Like questioning what your address is
10-001 (FRMR)
  Used to determine that a syntax error was encountered in the received frame.
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 54: Synchronous Protocols – Bit Oriented – HDLC Frame Structure – S-Frame – P/F (Poll/ Final)
P/F bit is always 1
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 55: Synchronous Protocols – Bit Oriented – HDLC Mechanism
I, U and S frames
3-phase mechanism
  One of the sides must install the link
    in order to be able to exchange data sequentially
  User data, flow and control information required for error control must be transferred between the two ends.
  One of the sides terminates the connection
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Bit stuffing: Bit doldurma

## Slide 56: Synchronous Protocols – Bit Oriented – HDLC Mechanism – Con’t
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5

## Slide 57: Synchronous Protocols – Bit Oriented – HDLC Mechanism – Multi-Point
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 58: Synchronous Protocols – Bit Oriented – HDLC Mechanism – Combined
BLM3051
Data Communication and Computer Network - 5
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 59: Thank you for your listening.
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 5