## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information
Course Hours: Tuesday 09:00 – 11:50
All courses will be face 2 face.
For announcements: https://avesis.yildiz.edu.tr/fcakmak/dokumanlar
  OBS Course/Bulk Messaging System
  Google Classroom Class Code: b5ggwqk
  You can ask your questions via Google Classroom
  Zoom Personal Room:
  https://us04web.zoom.us/j/3752287039?pwd=TTFKNittZWJTUEhHREovckl0VTVYUT09
  Meeting ID: 375 228 7039
  Passcode: 5AXMNd
For your questions and consultations about the course, make an appointment AT LEAST 1 (ONE) DAY BEFORE via the link below.
  https://fcakmak.simplybook.it/v2/
  No appointment will be made by e-mail.
  Please be at the above mentioned Zoom room at the appointment time.
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 1

## Slide 3: Lecture Information - 2
Students should ask the questions during the lesson out loud, NOT by writing.
The student who wants to ask questions must make himself/herself visible.
Students should keep their microphones OFF while listening, except when they ask.
In cases of possible long-term (> 1min) disconnection, the announcement regarding the continuation of the course will be made immediately on the Google Classroom page.
Students may record the lecture externally.
  Lecture presentations will NOT be shared.
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 4: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 1

## Slide 5: Lecture Information Form– Coursebook
 | Coursebooks
1 | Introduction to Data Communications & Networking, Behrouz Foruzan
2 | Computer Networks 2e, Andrew S. Tanenbaum
3 | Data Networks:Concepts, Theory and Practice, Uyless D.Black
4 | Routing & Switching: Time of convergence, Puzmanova
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 6: Lecture Information Form– Evaluation
Evaluation System | Method | # | Impact (%)
 | Midterms | 2 | 40
 | Quizs | - | -
 | Homeworks | - | -
 | Projects | 1 | 20
 | Semester Project | - | -
 | Laboratory | - | -
 | Other | - | -
 | Final Exam | 1 | 40
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 7: What is Communication?
Sharing information/data
Telecommunication (Tele -> far *Greek)
Communication Aim: Trafic data
Telephone, Television, vb.
  Ses, video, resim
Computer
  Medium/Media -> 0/1
Protocol Stack: Software and Hardware
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 8: What is Communication? – Con’t
Humanity History: 200k
Sumerians: B.C 4000
«Verba volant, scripta manent»
Copper Cable
  Telegraph: 1837-1838
  Telephone: 1876
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: Söz uçar, yazı kalır.
Bakır Kable

## Slide 9: Essentials of Data Communication
Message
Sender
Receiver
Medium
Protocol
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 10: Data Communication
Sender
Receiver
Medium
Message
Protocol
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 11: Data Comm. Features
Delivery
Accuracy
Timeliness
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 12: Pros of Computer Network
Resource Sharing
Info/Data Sharing
Load Sharing / Balancing
Reliability
Econmony
Efficient communication between in different places
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 13: Evaluation Criteria for Computer Networks
Performance
  Transmit time
  Response time
QoS
  Circuit-switched (Synchronous) Bit rate, Min Error Rate, Transmission Rate
  Packet-switched (Asynchronous)  Maximum Packet Size, Mean Packet Transfer Rate, Mean Packet Error Rate, Jitter, Mean Packet Transmit Delay
Reliability/Availability
  MTBF – Mean Time Between Failure
  Restoring Time
  5-9  99,999%
Security
Scaleable
Adaptable
  Software, Hardware
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 14: Network Standards
De Jure
  ISO (International Organization for Standardization)
  ITU (The International Telegraph and Telephone Consultative Committee)
  IEEE (The Institute of Electrical and Electronics Engineers)
  ETSI (The European Telecommunications Standards Institute)
  EIA (Energy Information Administration)
  TIA (Telecommunications Industry Association)
  ANSI (American National Standards Institute)
  TSE (Türk Standartları Enstitüsü)
  IETF (Internet Engineering Task Force)
De Facto
  QWERTY keyboards
  VHS video format
  PDF document type
  Buttons on men's shirts are on the right, buttons on women's shirts are on the left.
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 15: Computer Network (CN)
ARPANET (1970s)
Classification of CN
  Technique of Tranmission
    Broadcast
    Peer to peer – P2P
  Network Dimension
    PAN-Personal Area Network (< 10m)
    LAN-Local Area Network (< 100m-200m)
    CAN-Campus Area Network (< 1-5km)
    MAN-Metropolitan Area Network (< 10-50km)
    RAN-Regional Area Network (< 100-200km)
    WAN- Wide Area Network (< 1000km)
  Bit Rate
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 16: Topology
Bus
Star
Tree
Ring
Mesh
Hybrid
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 17: Bus Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 18: Star Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 19: Tree Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 20: Ring Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 21: Mesh Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 22: Hybrid Topology
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 23: Transmission Model
Simplex
  Mouse
  Bar Code Reader
Half-Duplex
  Radio
Duplex
  LAN
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 24: Addressing Model
Broadcast
  TV
Multicast
  Stream Video
Anycast
  DNS
Unicast
  Letter
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 25: Data Flow Density, Bit Rate, Throughput
Symmetric
Asymmetric
bps (bit-ps), Bps (Byte-ps)
  Kilo (k), Mega (M), Giga (G), Tera (T), Peta (P), Exa (E), Zetta (Z) ve Yotta (Y)
Throughput
Response time
Jitter
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 26: OSI Reference Model
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
ISO – 1984
De Jure
Features
  Open
  Flexible
  Robust
  Interoperable
  Easy to explain
  Easy to understand
7-layers
Never applied / Ideal Model
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 27: OSI Reference Model – Con’t
User
Support
Layers
Service
Layer
Network
Support
Layers
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 28: OSI Reference Model – Con’t
Each layers add a header package.
Only second layer (Data link) add a trailer end of the package.
  Error control
Encapsulation
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 29: OSI – Physical Layer
Responsible for trasmitting bit arrays between peers.
General functions of the Physical Layer;
  Electromechanic
  Direction of the package
  Determining magnitudes of signals
    Amplitude, Wavelength, Frequency
  Initiation and termination of the physical connection.
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 30: OSI – Data Link Layer
Extract/divide frames from the messages.
Send frames to receiver side in an order.
Using acknowledgment (ACK) info;
  In case of an error,
  In case of not receive the package,
  Re-transmission
Add header and trailer data to frames.
  To determine the starting and ending points of the frame.
Header includes;
  Sender address,
  Receiver address,
  Order info
Trailer includes;
  A code (to check errors)
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 31: OSI – Data Link Layer – Con’t
General functions of the Data Link Layer;
  Node to node error free delivery
  Addressing (in header part)
    MAC Address
  Access Control
  Flow Control
  Error Handling
  Synchronization
In Local Area Network (LAN)
  DLL divides into 2 different layers;
    LLC (Logical Link Control)
    MAC (Media Access Control)
Communication at the data link layer is in the same network.
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 32: OSI – Network Layer
Network layer is responsible for;
  Efficiently and accurately forwarding the packet
  From source to destination over different network links.
Communication at the network layer is in the different network
  Router (3rd level devices)
Switching
  Connection oriented
    like telephone infrastructure system
Routing
  Determining the path between sender and receiver
  Connectionless
    Delivering packages
  In DLL, data transfer occurs between nodes
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 33: OSI – Network Layer – Con’t
Address must be different from DLL’s addresses.
  Logical Address
Data transfer occurs between the source and the destination.
General functions of the Network Layer;
  Source to Destination packet delivery
  Logical addressing
  Routing
  Address transformation
    Between logical and physical addresses
  Multiplexing
    Multiple physical connections on a single newtwork connection at the same time
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 34: OSI – Transport Layer
Responsible for the transmission of data
  from source to destination
Network layer responsible for delivering data
Transport layer responsible for delivering packages
  data = package[]
Data transmission is between applications, not computers.
An additional addressing mechanism is required
  to distinguish the applications from each other.
  Service Access Point – SAP
    Ports, Sockets
Transport layer divides the incoming information into pieces (segment) in sizes supported by the infrastructure.
  Segmentation
    Sequence number
    Re-assembly
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 35: OSI – Transport Layer – Con’t
There are two types of services.
  Connectionless
    Like post services
  Connection oriented
    Like phone services
      Establish connection
      Data transmission
      Terminate connection
    More control over the data to be transferred
General functions of the Transport Layer;
  Data transmission between source and destionation nodes
  To provide data flow between applications with the help of service points
  Segmentation & Re-assembling
  Ensuring connection control
    Connectionless | Connection oriented
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 36: OSI – Session Layer
This layer is responsible for ensuring continuity.
  Synchronization
Choosing connection type
  Half-duplex
  Duplex
Session data transfering
  Password
  Logon verification
Sessions can be split into sub-sessions to ensure the reliability of the connection
Sub-sessions are provided with checkpoint information.
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK
Notes: MTBF – Mean Time Between Failure -> Hata Oluşma Sıklığı

## Slide 37: OSI – Session Layer – Con’t
General functions of the Session Layer;
  Managing the session
  Communication control
    if it is half-duplex
  Ensuring synchronization
  Gracefull close
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 38: OSI – Presentation Layer
General functions of the Presentation Layer;
  Provides interoperability by eliminating possible differences in information representation between devices during data communication
    Abstract data syntax
  Encryption & Decryption
  Compression & Decompression
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 39: OSI – Application Layer
User Interfaces
  Electronical mail (e-mail)
  File transfering
  Remote desktop control
  Internet explorer
  vb.
7 | Application Layer
6 | Presentation Layer
5 | Session Layer
4 | Transport Layer
3 | Network Layer
2 | Data Link Layer
1 | Physical Layer
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 40: Other Network Models
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 41: Thank you for your listening.
BLM3051
Data Communication and Computer Network - 1
Dr. Öğr. Üyesi Furkan ÇAKMAK